## Slide 1
C PROGRAMMING PROJECT REVIEW
Smart Physiotherapy
Assistant
Arduino-based joint movement tracking to guide and log physiotherapy exercises
Team Name | Domain: Embedded Systems / Healthcare Tech | Language: C

## Slide 2
Problem Statement
01
No continuous, quantifiable record
Manual tools (goniometers, therapist observation) give a single subjective reading and leave no continuous log of joint range of motion between clinic visits.
02
Naive sketches don't scale to long sessions
Memory-heavy constructs (String concatenation, unbounded arrays) fragment the limited SRAM (2KB on an Arduino Uno) if a session runs for many samples.
03
No real-time safety fail-safe
Without an immediate alert, a patient can overextend a joint during an unsupervised exercise and risk re-injury before anyone notices.
04
The need
A lightweight, C-native system that computes joint angle in real time, persists history without heap allocation, and gives instant threshold-based feedback.
Smart Physiotherapy Assistant
2

## Slide 3
Proposed Solution
An Arduino-based wearable/attachable unit that senses joint movement, gives instant feedback, and keeps a digital record of every session.
Tracks real-time elbow / knee bend angle using an MPU6050 sensor
Detects a full repetition (extend → flex → extend) and counts it automatically
Buzzer + LED alert the patient the moment a movement crosses an unsafe threshold
Stores each session's min / max / average angle for progress comparison
Entire system is built and demonstrated as a simulation on Wokwi
Sense
MPU6050 reads joint angle
Process
Arduino computes angle & checks threshold
Alert
Buzzer / LED feedback in real time
Log
Session data saved for review
Smart Physiotherapy Assistant
3

## Slide 4
Feasibility of the Idea
Smart Physiotherapy Assistant — grounded in low-cost, well-documented components and a simulation-first build
1
Technical
Uses standard, well-documented parts (Arduino Uno, MPU6050) with mature C libraries — no exotic hardware or custom silicon needed.
2
Economic
All components are low-cost and widely available; the simulation-based build removes hardware cost entirely for this review stage.
3
Implementation
Single microcontroller, single sensor pipeline — fits comfortably within a C course project's timeframe and complexity target.
4
Scalability
The enum-based body-part design and modular functions let the same code extend to more joints or add wireless logging later.
Smart Physiotherapy Assistant
4

## Slide 5
C Concepts Used
Every core feature is a deliberate showcase of a fundamental C concept
Structs
Grouping related session data (angle, timestamp, rep count, patient ID) into a single organized memory block
Pointers
Passing session data by reference into logging/threshold functions, avoiding costly struct copies
Enums & Switch-case
Representing body part and session state (ELBOW, KNEE, IDLE, ACTIVE) without magic numbers, dispatched in the main loop
Circular buffers (Arrays)
Maintaining a rolling log of the last N angle samples using modulo arithmetic instead of unbounded storage
Loops
Continuous sensor polling and edge-detection logic used to count a full extend-flex-extend rep
EEPROM (native file I/O)
Persisting the calibration baseline and session summaries across power cycles with no heap allocation
Macros (#define)
Fixing threshold angles, pin numbers, and buffer sizes at compile time instead of runtime constants
Static/global vars
Tracking the session counter and lifetime rep total across loop iterations
Recursion
Computing the recursive min/max across a session's angle log
Sorting/searching
Ranking stored sessions by best/worst range of motion for the summary report
Bitwise operations
Packing status flags (calibrated, threshold breached, session active) into a single byte
C-strings (char[], string.h)
Safe, stack-based formatting of the serial menu and CSV-style export lines
Smart Physiotherapy Assistant
5

## Slide 6
System Workflow
Sensor Reads
Angle (MPU6050)
Arduino Computes
Joint Angle
Threshold Check
(safe / unsafe)
Feedback
(LED + Buzzer)
Log Session
(EEPROM / SD)
A continuous loop: every exercise repetition is sensed, evaluated against a safe range, and immediately reflected back to the patient — with a permanent record kept for the next session.
Smart Physiotherapy Assistant
6

## Slide 7
Tools & Requirements
Hardware Components
Arduino Uno (simulated)
MPU6050 accelerometer + gyroscope
Push button — calibration trigger
Buzzer + LED — safety alert
16x2 LCD — optional live readout
Software / Environment
Wokwi Online Simulator
Arduino IDE (code authoring)
Core Libraries
Wire.h — I2C communication
MPU6050.h / Adafruit_MPU6050
native EEPROM.h — persistence
LiquidCrystal.h — LCD output
Smart Physiotherapy Assistant
7

## Slide 8
Expected Output
1
Real-Time Angle Readout
Live joint angle value streamed to the Serial Monitor (or LCD) throughout each exercise
2
Automatic Rep Counter
Every full extend-flex-extend cycle detected and tallied without manual input
3
Threshold Safety Alert
Immediate buzzer + LED warning the instant a movement exceeds a pre-defined safe angle
4
Session Summary Report
Min, max, and average angle computed and displayed at the end of each session
5
Persistent Session History
Past session data retained across power cycles (EEPROM) and retrievable via the serial menu
6
Progress Trend Export
CSV-style log of stored sessions, showing whether range of motion is improving over time
Smart Physiotherapy Assistant
8

## Slide 9
Conclusion & Future Scope
The Smart Physiotherapy Assistant demonstrates how core C programming concepts — structs, pointers, enums, file I/O, and more — combine to build a genuinely useful embedded system.
Extend tracking to multiple joints simultaneously (shoulder, wrist, ankle)
Add wireless (ESP8266) logging to a companion mobile app
Cloud-based storage for therapist review across sessions
Basic trend analysis / ML-based movement quality scoring
Thank You